## Slide 1: Are biosurfactant and chelating agent mixtures good additives for electro-kinetic remediation of multi-contaminated sediments?
Sediment information
Y. Tian1,2, F. Portet-Koltalo1, A. Benamar2, C. Boulangé-Lecomte3
Laboratory COBRA UMR CNRS 6014, University of Rouen, 55 rue Saint Germain, 27000 Evreux, France. Yue.tian@etu.univ-lehavre.fr
Laboratory LOMC UMR CNRS 6294, University of Le Havre, 53 rue Prony, 76058 le Havre, France. 3 Laboratory SEBIO UMR I02, University of Le Havre, 25 rue Philippe Lebon, 76058 Le Havre, France
Why this study ?
  Many organic pollutants such as PAHs, PCBs and metal contaminants are cumulated in dredged sediments which are immobilized in deposit areas with no possible valorization.
  Specially, the sediment of Seine River at Tancarville (Normandy, France) is rich in clay, carbonates and organic matters which make the sediment difficult to be treated for remediation.
  Consequences:
  Damage to aquatic ecosystems, possible transfers (groundwater)
  Toxic for living organisms including human-beings
  Aims of researches :
  Enhancing electro-kinetic remediation
  Using combinations of biodegradable surfactants and chelating agents
Harbor dredged sediments
    Rich in clay, carbonates (pHsediment=8.4) and organic matter (OM6%)
    High retentive power for metals (clays) and organic contaminants (OM)
    Buffer effect (carbonates) : Reduce metal mobility
Chart: PAHs and PCBs extracted from Tancarville sediment
| naphtalène | acénaphtène | acénaphtylène | fluorène | phenD10 | phénanthrène | anthracène | fluoranthène | pyrène | benzo(a)anthracène | chrysène | benzo(b)fluoranthène | benzo(k)fluoranthène | benzo(a)pyrène | PerD12 | indeno(1,2,3,cd)pyrène | dibenzo(a,h)anthracène | benzo(ghi)pérylène | PCB 28 | PCB 52 | PCB 101 | PCB 153 | PCB 138 | PCB 180 | PCB 209
 | 3.8848 | 31.0725 | 26.473 | 63.0201 | 159.4917 | 114.3154 | 242.3418 | 232.6552 | 138.8952 | 130.5953 | 308.4202 | 107.9851 | 157.9453 | 137.1694 | 36.1243 | 126.904 | 0 | 0 | 10.9045 | 32.0369 | 22.5743 | 18.0726 | 0
> Level 1 (GEODE)
> Level 2 (GEODE)
Heavy metals extracted from Tancarville sediment
Electro-kinetic remediation
2 dominant processes :
Electro migration
Electro osmose
Objective:
  Desorb, solubilize the pollutants in sediment pores and transport them toward the electrodes by applying an electric field (1 V/cm)
Advantages:
  For low permeability sediment
  Multi-decontamination
  Fast
  Site implementation
  Difficulties: suitable efficient additives
  Maintain pH: acid
  Solubilize lipophilic compounds
  Transport heavy metals
  Environmentally friendly treatment
Good chelating agent
Maintain pH ≈ 4
Natural molecule
Biosurfactants
  Non toxic, Biodegradable
Solubilize PAHs, PCBs, etc.
Enhancing Additives
Citric acid
Rhamnolipid
Saponin
anionic
nonionic
12-days treatment : Mixing citric acid + Rhamnolipid (biosurfactant)
(periodic voltage: 5 days on/2 days off, energy savings)
Chart: Variation of electric current
| 0 | 24 | 48 | 73 | 97 | 120 | 121 | 167 | 168 | 192 | 217.45 | 240 | 263 | 288
 | 26.7 | 11.89 | 7.65 | 5.2 | 5.25 | 12.4 | 0 | 0 | 13.3 | 11.72 | 12 | 12 | 13.6 | 12.9
Chart: Variation of pH of treated sediment
| 0.125 | 0.375 | 0.625 | 0.875
 | 2.85 | 3.56 | 5.93 | 6.43
“Flush” effect of periodic voltage on I : not very pronounced
Acid maintenance successful
    But pH> pKaRhamnolipid ~ 4.8, Rhamnolipid: anionic  migrate s to anode (opposed to EOF) detrimental for removing organics?
PAHs, PCBs: migrate from middle to anode
  poor removals for PAHs
  no removals for PCBs
Problem with the anionic biosurfactant?
Chart: Variation of PAHs concentrations
| 0.125 | 0.375 | 0.625 | 0.875
phenanthrene | 2715.2812 | 2585.7616 | 2556.2174 | 2541.5023
fluoranthene | 2733.0365 | 2434.1242 | 2470.3391 | 2529.7523
pyrene | 2445.8096 | 2126.0318 | 2228.5857 | 2250.6704
chrysene | 2965.7668 | 2638.1578 | 2793.5633 | 2834.41
benzo(a)pyrene | 1596.3301 | 1267.769 | 1487.9882 | 1506.7407
initial phenanthrene | 2496.8033 | 2496.8033 | 2496.8033 | 2496.8033
initial fluoranthene | 2500.318 | 2500.318 | 2500.318 | 2500.318
initial pyrene | 2262.9085 | 2262.9085 | 2262.9085 | 2262.9085
initial chrysene | 2818.7851 | 2818.7851 | 2818.7851 | 2818.7851
initial benzo(a)pyrene | 1501.7925 | 1501.7925 | 1501.7925 | 1501.7925
Chart: 5 heavy metals in different sections
| 0.125 | 0.375 | 0.625 | 0.875
Cr2677 | 57.372 | 224.7223 | 260.0261 | 87.215
Cd2265 | 0.97416 | 17.1009 | 40.0452 | 14.6055
Cu3273 | 32.2682 | 133.764 | 114.1079 | 73.0402
Pb2203 | 44.177 | 228.7373 | 171.3914 | 143.5813
Zn2025 | 31.0197 | 283.0915 | 764.1628 | 416.5776
initial Cd | 21.9587 | 21.9587 | 21.9587 | 21.9587
initial Cr | 191.2905 | 191.2905 | 191.2905 | 191.2905
initial Cu | 94.3612 | 94.3612 | 94.3612 | 94.3612
initial Pb | 151.1995 | 151.1995 | 151.1995 | 151.1995
initial Zn | 502.8555 | 502.8555 | 502.8555 | 502.8555
Heavy metals: migration only begins
  Poor removals (1-18%)
Not enough time to migrate more to the electrodes?
Chart: Time (h)
| 0 | 1.5 | 24 | 48 | 72 | 96 | 120 | 144 | 167 | 168 | 192 | 216 | 240 | 288 | 312 | 335 | 360 | 384 | 408 | 432 | 480 | 503 | 504 | 552 | 576
CA+rhamno | 8.4 | 7.5 | 5.4 | 8.6 | 9.2 | 9.8 | 13.7 | 0 | 0 | 14.9 | 16.9 | 19.6 | 15.7 | 11.7 | 0 | 0 | 14.7 | 12.2 | 20.5 | 21.3 | 0 | 0 | 20.9 | 20.2 | 18.4
CA+viscosin | 26.4 | 35.1 | 20.1 | 11.3 | 8.3 | 0 | 0 | 26.1 | 15.7 | 10.8 | 9.5 | 7 | 0 | 0 | 21.4 | 10.1 | 9.2 | 9.9 | 0 | 0 | 14.3 | 12.2 | 12.2
PAHs remediation by 2nd treatment
Need longer-time treatment
24-days treatment : Citric acid + Rhamnolipid or viscosin-like biosurfactants
(periodic voltage: 5 days on/2 days off, energy savings)
“Flush” effect of periodic voltage on I : more important
PAHs depletion at cathode side
  Better removals (-25%)
Heavy metals:
  Cd, Pb, Zn: better removals than 1st test (11-34%)
Citric acid + Tween 20
Citric acid + SDS
Citric acid + Tween 20: better removals for PAHs
  Anionic surfactant SDS moves against EOF detrimental for removing organics
Anionic or nonionic surfactants ?
  Citric acid + nonionic Tween 20 or Citric acid + anionic SDS, 12 days treatment
Possible improvements Conclusion
Testing saponin (nonionic biosurfactant) instead of rhamnolipid
Higher saponin concentration (biodegradability: regular renewal)
Longer treatment time for clay and carbonate rich sediments
Mixtures of biodegradable chelating agents + biosurfactants
Promising candidates for EK multi-decontamination
Tests with a chelating agent and a surfactant
Electroosmotic flow
(EOF) +
Evacuation of gas
Pump
Balance
Sediment sample